MPPT Overview

Main features
- Accept PV input up to 50V and 15A (500+W). Start with 36V Max (limit is IN226). Diode prevents back feed of PV (is a MOSFET, so can be overridden).
- Two bi directional buck/boost stages (green hexagons). Boost towards power node, buck towards battery.
- Power node runs at wired-OR voltage of PV and both batteries.
- Battery to battery charging capability by source battery boosting to power node voltage.
- Current/voltage monitoring of all inputs/outputs using INA226s on shared I2C line
- LCD output
- 2x control buttons
- 1x rotary encoder (+ push) = 3 GPIO
- USB CDC debug port.
- CAN port
- 2x control inputs (ADC)
- Thermistor on heatsink. (ADC)

Main parts
- CH32V203C8T6 microcontroller at 96 or 144MHz.
  - Gives wide PWM range.
  - Rich peripherals
  - RISCV, 64kB flash, 20kB RAM.
- INA226 current/voltage monitoring at approx 2 sec sampling interval. Common I2C bus.
- MOSFET drivers
- MOSFETS
- Thermistor
- LCD
  - 74HC595 serial in parallel out for IO expansion.
- EEPROM (128kbytes?)

Peripherals used
- GPIO
  - Out
    - 3x LEDs
    - Fan enable
    - PV FET enable
  - In
    - 2x push switches
    - 1 x button
    - Rotary encoder + push (3 inputs)

- TIM1: Timer with deadband etc and 4 PWM channels.
  - 2x PWM control channels for switchers. (4 pins)
- I2C1: (using DMA Channel 6 TX & Channel 7 RX).
  - INA226 monitoring
  - EEPROM
- ADC1:
  - Node voltage,
  - 2x control inputs,
  - thermistor
  - Maybe inputs if needed (R2R)?
- CAN
- LCD via 74HC595
  - 4 bits data
  - RS (only needed if special chars are used)
  - E
  - LED control
  - NB: R/W is NOT needed. Tied to GND. Write only.
- LCD PWM for contrast.
- USB CDC (debug?)
- UART3 for debug output (TX only, DMA)

### Peripheral Pins
Peripheral	Pins	Pin Name	DMA	Comment
SWD	34, 37	PA13, PA14		Debug
TIM1_BKIN	25	PB12		Needed?
TIM1 CH1	29	PA8		PWM1 H
TIM1CH1N	26	PB13		PWM1 L
TIM1CH2	30	PA9		PWM2 H
TIM2CH2N	27	PB14		PWM2 L

CAN	45, 46	PB8, PB9

TIM3	19	PB1		LCD Contrast

I2C1	42, 43	PB6, PB7	6, 7	INA226 x3, EEPROM

USBD	32, 33	PA11, PA12		CDC port

USART3	21,22	PB10,PB11	2,3

ADC			1
ADC		PA0		Node voltage
ADC		PA1		Thermistor
ADC		PA2		Ctl input
ADC		PA3		Button/Switch R2R

Unassigned		PC13
Unassigned		PA4

#### GPIO Assignments
Panel Diode bypass	Out	PA5
Fan out	out	PB15
Exp Data	out	PB5
Exp Serial Clock	out	PB4
Exp Out Clock	out	PB3
Debug LED0	out	PA15
Debug LED1	Out	PB0

Rotation A	In	PA6
Rotation B	In	PA7

### R2R Switches
Sw 0	In
Sw 1	In
Rotation press	In
Button press	In

### Expansion Output via 74HC595s
LCD D4
LCD D5
LCD D6
LCD D7
LCD RS
LCD E
LCD Backlight